## Slide 1
Stability at low sampling rates and high stiffnesses
Indrajit Desai and Abhishek Gupta (Mechanical Eng.)
and
Debraj Chakraborty (Electrical Eng.)

## Slide 2: Big Picture
Demands from the Networking Engineer
Control Engineer
Demands from the User

## Slide 3: The “wall” in haptics
A wall is the basic construct in haptics.
Most solid shapes are made of (tiny) walls.
Virtual Wall
(from www.coolwearables.com)
Our primary devices

## Slide 4: User Req. 2: The wall should feel like a spring
The wall is a (stiff) spring
y
We want:
No force
Fh = - ky
Then the user will feel just the spring and not the device he is actually holding
Unfortunately this is not completely possible
y
y
Virtual Environment
wall
Free
space
controller
Measured
Motor

## Slide 5: Instead of a spring we get
The wall is modeled as a (stiff) spring
Virtual Environment
Haptic Device
Controller
Fh
Fu
The control problem in haptics: It is the job of the controller (Fu ) to change the above equation into
Fh = - ky
y
y
Virtual Environment
wall
Free
space
controller
Measured
Motor

## Slide 6: User requirement 1: Stability of the Wall
The Fh to x map must be stable (BIBO) always: In free space, at the interface and inside the wall
+
-
Haptic Device
Controller
Human force input
Device displacement
The controller is chosen based on the value of x (switching controller!)
wall
Free
space
Virtual Environment
controller
Measured
+
-
Device
Dynamics
wall
Free
space
Virtual Environment
controller
Measured
Controller knows the wall position

## Slide 7: Implementation and Networking requirement:(Slow) Sampling
+
-
Haptic Device
D/A
Digital Controller
A/D
Human force input
Device displacement
Sampling time T
Conventional control theory advices sampling at least 2-3 times the system bandwidth
System BW depends on the users specs and consequently the controller we design
Human force input is limited to 6Hz (sometimes 10Hz)
Human sensory BW is much higher 200-300Hz
Most commercial devices have decided to sample at 1000Hz
Actuator Force feedback

## Slide 8: Slow Sampling is even more crucial in tele-haptics (no results yet)
As explained before: low sampling rates (i) bring down cost, same channel can be used for other purposes
Tele-haptics also demands tolerance to large delays (not yet studied by us)

## Slide 9: Big Picture
Demands from the Networking Engineer
Low sampling rates (40Hz)
Large delay tolerance
Control Engineer
Demands from the User
Stability (safety) (100Hz)
Fast tracking of force commands (6Hz)
Real feel of the specific environment (300Hz)
Numbers given are for quick understanding and estimates: the actual values depend on many design parameters
Play safe at 1000Hz

## Slide 10: The most common haptic controller
Open Loop Impedance Control (OLIC)
+
-
Haptic Device
D/A
Environment to be simulated
A/D
Human force input
Device displacement
Sampling time T
+
-
H(s)
ke
F_h
y
Improper way to write
The poles go outside the unit circle with increasing sample time at around 100Hz (for this specific example)
Colgate (1997) derived a passivity based stability criterion:

## Slide 11: Our Method: (Old) Model matching theory in a virtual reality wrapping
We noticed that the two user requirements of (a) mimicking a given system (b) while preserving stability is exactly the H-infinity model matching problem.
The requirements above are:
E(s) and the closed loop system G(s) must match for a large range of input frequencies
C(s) must be stabilizing i.e. G(s) must be stable

## Slide 12: Model Matching Approach
Given a error tolerance of g H-infinity model matching theory lets us efficiently search for a stabilizing controller C(s) such that
Clearly such a controller will not exist
Hence we bring in a weighting function of cutoff freq wc and solve for C(s) using the following constraint
the BW achieved can be made to be larger
than wc

## Slide 13: Model Matching Approach offers flexibility
P1: Given a error tolerance, we can search for the maximum BW achievable while preserving stability
P2: Given a required BW, we can search for the minimum error achievable for all frequencies up to the BW.
P3: Given a error tolerance and acceptable minimum BW we can try to search for controllers at various sampling rates

## Slide 14: Peaucellier Mechanism Setup
(such a indigenous setup is required since the commercial devices (Phantom) do not allow us to change the sampling rate

## Slide 18
Thank You