## Slide 1: EE204: Analog Circuits
Sandip Mondal
Assistant Professor IIT Bombay
Lecture-11

## Slide 2
2
What is the function of diode D2 ?

## Slide 3
3
Use of D2
+12V
Relay has 100mA current with 15V supply
The resistance of the coil = = 120 Ohm
Energy stored in the inductor =
Switch

## Slide 4
4
Use of D2
When we switch OFF the transistor, the current flowing through the transistor will be OFF.
When current was flowing through the coil, a magnetic field generated in the coil and the energy () is align towards magnetic field.
After switching OFF the transistor, the current flow through inductor will be interrupted. Hence current will start decreasing through inductor.
Decreasing current will produce decreasing magnetic field.
Decreasing magnetic field will induce voltage in the coil. (it is a self induce coil)
The polarity of the induced voltage will be adding to input voltage
+12V
0V

## Slide 5
5
Use of D2
The voltage at point C is sum of the imput voltage and induced voltage (L)
Assume: L=50 mH, and we know i=100mA and t=1us. (slide No 17).
Then induced voltage = 50 = 5000V
Hence 5000V at point C will break the transistor
Hence we need to use diode to pass the current at OFF condition of the transistor
0V
+12V
L
C

## Slide 6
6
Use of D2
Diode operating voltage is 0.6V and C point can’t increase beyond 12.6 voltage.
The current will flow across the diode-inductor loop and heat will dissipate through this.
The transistor will not be destroyed.
+12V
0V
C

## Slide 7
7
Transistor Relay Circuit

## Slide 8
8
Transistor Relay Circuit
Conditions:
of the OPAMP is +15V, relay to be ON
of the OPAMP is +15V, relay to be ON
+12V
-15V
+15V
We need to find and ?

## Slide 9
9
We need to find and ?
+12V
-15V
+15V
In order to find and , we need to find base current.
To find base current we need to obtain collector current.
Collector current is nothing but the load current relay current
Relay current will be given by the manufacturer.
Assume: Relay current = 100mA
Once relay current is known then the = 100mA
Base current: = =1mA (Assume: =100)
We know if transistor is on then the base voltage would be 0.6 V
1mA
0.6V

## Slide 10
10
We need to find and ?
+12V
-15V
+15V
In is used to discharge the base emitter capacitance of the transistor while no output available from D1 and OPAMP will be in negative saturation state.
The can be large as the base emitter capacitance approximate 100pF.
If = then OFF time = R×C= =
Current through =
=1mA and . Hence the total current flowing through =1.06mA
Now we need to find voltage drop across
1mA
0.6V

## Slide 11
11
We need to find and ?
+12V
-15V
+15V
Voltage drop across = 15V ─ 1.2V (Two diode loss in the OPAMP) ─ 0.6V ( loss) ─ 0.6V (Voltage at base of Transistor) = 12.6 V
Current through ==
so that even if the temperature is high so that it can supply the current, hence to be considered =
1mA
0.6V
13.8V
13.2V
Comparator

## Slide 12
12
Relay Drive using MOSFET

## Slide 13
13
MOSFET equivalent ckt
+12V
-15V
+15V
The output voltage after the D1 is 13.8V that is sufficient to drive the MOSFET (No need to worry for current)
13.8V
13.3V
MOSFET

## Slide 14
14
MOSFET equivalent ckt
+12V
-15V
+15V
When there is a output voltage from the OPAMP of -13.8V then there is no output from D1.
But was charged during positive voltage (+13.8V) and hence there is no discharging path. Hence we need to a resister to discharge the
-13.8V
MOSFET
0V

## Slide 15
15
MOSFET equivalent ckt
+12V
-15V
+15V
When there is a output voltage from the OPAMP of -13.8V then there is no output from D1.
But was charged during positive voltage (+13.8V) and hence there is no discharging path. Hence we need to a resister to discharge the
Time constant during switching OFF time, R×C= × = (if R=10k)
-13.8V
MOSFET
BS-170
0V

## Slide 16
16
Disadvantage MOSFET Switch
+12V
-15V
+15V
Designing of MOSFET switch is easy but limited with high voltage operation.
BS-170 operates with 5V only.
If any circuit needs to be operated at low voltage (say +/- 2V) then the MOSFET circuit will not work for such operation.
Where the transistor require only 0.6V base-emitter voltage to operate in the transistor.
-14.2V
MOSFET
BS-170
0V