## Slide 1: EE204: Analog Circuits
Sandip Mondal
Assistant Professor IIT Bombay
Lecture-4

## Slide 2
2
What is the problem with this circuit?
LED On/Off using electronic circuit
+15V
LED

## Slide 3
3
For most of the LED required only 1.8V to glow and 10mA current
LED On/Off using electronic circuit
+15V
LED
If you apply 15V, an enormous current will flow through the LED, and it goes bad.
We should be aware of basic rule of design

## Slide 4
4
The voltage drop across 1.8V
The remaining voltage of 13.2 will drop across R.
If 10mA current flows through the circuit, then the R=13.2V/10mA=1.32kΩ ~ 1.5KΩ
LED On/Off using electronic circuit
+15V
R
LED

## Slide 5
5
If I have 15V supply in the base, then what will be the resistance value of R1 ?
How to use the Transistor to LED to glow ON/OFF
+15V
R
LED
+15V
R1

## Slide 6
6
The base needs some current. Now we need to find the
How to use the Transistor to LED to glow ON/OFF
+15V
R
LED
+15V
R1
To find the base current what is the parameter we should know?

## Slide 7
7
𝛃 = 100
How to use the Transistor to LED to glow ON/OFF
+15V
R
LED
+15V
R1
= 10 mA required to glow the LED
= / 𝛃 = 0.1 mA
0.1 mA
B
C
E
The voltage at E=0V hence voltage at B=0.6V required to conduct the Transistor

## Slide 8
8
How to use the Transistor to LED to glow ON/OFF
+15V
R
LED
+15V
R1
0.1 mA
B
C
E
What is the value of R1 ?

## Slide 9
9
How to use the Transistor to LED to glow ON/OFF
+15V
R
LED
+15V
R1
0.1 mA
B
C
E
The voltage at E=0V hence the voltage at B=0.6V required a transistor to conduct.
The voltage across the R1 should be 15-0.6 = 14.4 V
The current is 0.1mA
Hence the resistor R1 should be 14.4V/0.1mA = 144 kΩ
3019

## Slide 10
10
Circuit – ON/OFF

## Slide 11
11
Circuit – ON/OFF
Transistor
LEDs
ON
ON
OFF
OFF

## Slide 12
12
Bias compensation with diode
Input
Signal
Working mechanism ?
Advantages?
Disadvantages?

## Slide 13
13
Bias compensation using a Thermistor
Input
Signal
Working mechanism ?
Advantages?
Disadvantages?

## Slide 14
14
Concept Question
1) Please design NOT, NAND and OR gate using maximum three transistors.
2) Prove the Boolean algebra and truth table