## Slide 1: EE204: Analog Circuits
Sandip Mondal
Assistant Professor IIT Bombay
Lecture-9

## Slide 2
2
Voltage regulator
Let's assume 20V DC is the un-regulated input varied anywhere between 28 V to 15V
Input 20V DC (15V20V28V)
We want output =10V (steady)
How this circuit works?

## Slide 3
3
Voltage regulator
If I remove all connections !
Input 20V DC (15V20V28V)
How much current needs to flow through Zener? How can we find that?
This is biasing the Zener
5V
Assumed 5V Zener. If sufficient current flowing through it, then there will be voltage drop of 5V.

## Slide 4
4
Voltage regulator
10mA is the knee current of Zener diode then only voltage drop will be 5V across Zener diode
P
Input 20V DC (15V20V28V)
Data sheet to the Zener Diode
This is biasing the Zener
5V
We know the voltage at point P is never going to be below 15V
Hence there is minimum 10V drop across
If and 10mA current flows through this, then the voltage drop will be 10V

## Slide 5
5
Voltage regulator
If the input voltage increase to 28V then more current will flow through , and more voltage drop across it. More current will be flowing through Zener and slight increase in Zener voltage which is harmless.
P
Input 20V DC (15V20V28V)
This is biasing the Zener
5V

## Slide 6
6
Voltage regulator
The registerand are used as a volage divider. It will give the divided voltage at point Q
P
Input 20V DC (15V20V28V)
This is biasing the Zener
5V
Q
If we use and, then the voltage at Q would be 5V.
Now if we add transistor?

## Slide 7
7
Voltage regulator
The E1 point will be always sitting at 5V
Input 20V DC (15V20V28V)
What happened if the output voltage increases more than 10 V?
P
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2

## Slide 8
8
Voltage regulator
If E1 is at 5V then B1 should be 5.6V
Input 20V DC (15V20V28V)
P
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
If B1 increase more than 5.6V then T1 will conduct heavily through PSC1
S
Then the voltage drop across will increase
The voltage at point C1=Voltage at P – Voltage drop across
Voltage at E2 =Voltage at C1-0.6V

## Slide 9
9
Voltage regulator
Assume P is sitting at 20V at any given time.
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
Assume k
S
k
If 4mA goes through then drop across is 20V then C1 will be sitting at 0V
If 1mA goes through then drop across is 4.7V then C1 will be sitting at 15.3 V
If 2mA goes through then drop across is 9.4V then C1 will be sitting at 10.6 V

## Slide 10
10
Voltage regulator
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
S
k
If 2mA goes through then drop across is 9.4V then C1 will be sitting at 10.6 V and E2 will be at 10V=
Voltage at E2 =Voltage at C1-0.6V
If more B1= more than 5.6V then more current flows through that will make the voltage decrease at C1 hence decrease in voltage at E2 and
Hence voltage at Q will decrease

## Slide 11
11
Voltage regulator
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
S
k
B2 point is less than 5.6 V
The current through will be less
The T1 will conduct less
Voltage drop across reduce
The voltage at C1 will increase
The voltage at E2 will increase
The voltage at Q will increase
The T1 will conduct high

## Slide 12
12
Voltage regulator
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
S
k
If I vary resistance the is changing
Nevertheless will be always constant
will be always constant with respect to

## Slide 13
13
Voltage regulator
What are the drawbacks of this voltage regulator?

## Slide 14
14
Voltage regulator
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
S
k
At 65C, only
Base emitter temperature drift
E1 =5V , so B1= 5.5V, =11 V
Hence the output is changing with respect to temperature

## Slide 15
15
Voltage regulator
Input 20V DC (15V20V28V)
P=20V
This is biasing the Zener
5V
Q
T1
T2
E1
B1
C1
B2
E2
C2
5.6V
5V
S
k
If the supply voltage become high hence P=30V
Change in supply voltage
C1 =11.2V hence drop across must 18.8V
If the supply voltage become low hence P=15V
C1 =11.2V hence drop across must 3.8V
More current =More (T1)
Less current =Less (T1)
Then the output voltage will change