## Slide 1: EE204: Analog Circuits
Sandip Mondal
Assistant Professor IIT Bombay
Lecture-16

## Slide 2
2
Temperature Indicator
IC sensor LM335
Temperature co-efficient of = -2.2mV / °C
At 25°C
= 0.6V
At 35°C
= 0.578V
LM335

## Slide 3
3
LM-335 Temperature sensor
LM335
+15V
1 mA
R
Min. current should be 1 mA. However you can send upto 10mA
What is value of R?
Lets assume operation temp is from 0C to 100C
The operation temperature = 10mV / °K
At 0°C voltage across the sensor (Vo) would be = 2.73 V
At 100°C voltage across the sensor(Vo) would be =(273+T°C )x10mV
= 3.73 V
(0°C corresponds to 273K)
At 25°C voltage across the sensor(Vo) would be =(273+25 )x10mV
= 2.98 V
(Complex number)
Vo

## Slide 4
4
Circuit requirement
LM335
+15V
3.73 V at 100°C
R
We need to construct a circuit which will offer 0C to 0V and 100C to 1.000V. How to achieve this ?
Using OPAMP
15-3.73=11.27 V
Lets consider 2mA current flowing through the circuit. Then the resistance R =

## Slide 5
5
LM335
+15V
R
=100k
DISPLAY
00V to 1.00 V
2.73V
At 0C output = 0 =(V1+V2)
At 100C output = -1.00 (V1+V2)
Circuit requirement

## Slide 6
6
LM335
+15V
R=5.6K
=100k
DISPLAY
00V to 1.00 V
-2.73V
At 0C output = -0.23 =(V1+V2)
What happened if V2 is not stable ?
-15V
LM336
-2.5V
But we need output would be 0V at 0C

## Slide 7
7
LM335
+15V
R=5.6K
=100k
DISPLAY
00V to 1.00 V
-2.73V
If we change the value of R1 then Output will be
Changing the value of R1
-15V
LM336
-2.5V

## Slide 8
8
LM335
+15V
R=5.6K
=100k
DISPLAY
00V to 1.00 V
-2.73V
If we change the value of R1 then Output will be
Using R1 + Pot at 0C
-15V
LM336
-2.5V
Pot=P1

## Slide 9
9
LM335
+15V
R=5.6K
=82k
DISPLAY
00V to 1.00 V
-2.73V
Gain of the system should be changed
Using R1 + Pot Rf at 100°C
-15V
LM336
-2.5V
Pot=P1
Pot=P2=22k

## Slide 10
10
LM335
+15V
R=5.6K
=82k
DISPLAY
00V to 1.00 V
-2.73V
Put LM335 in ice and adjust P1
Put LM335 at 100C and adjust P2
How to adjust?
-15V
LM336
-2.5V
Pot=P1
Pot=P2=22k
Perform this for few times.

## Slide 11
11
LM335
+15V
R=5.6K
=82k
DISPLAY
00V to 1.00 V
-2.73V
Put LM335 in ice and adjust P1 and adjust output to 0 V
Put LM335 at 100C and adjust P2 output to 1V
Repeat above steps for several times
How to perform the calibration
-15V
LM336
-2.5V
Pot=P1
Pot=P2=22k

## Slide 12
12
What is the temperature range ?
-20°C to 80°C = 100C
What is the error in the output if LM336 changes with respect to temperature
Ambient temperature change = 100C (Industrial grade equipment)
Temperature drift = 30x100 PPM =
The original voltage = 2.5V
The change for 2.5V for ΔT = 100C =
The Z